## Slide 1: When I use a word, it means just what I choose it to mean neither more nor less
LEWIS CARROLL , Through the Looking-Glass,

## Slide 2: 35.6kJ L-1
SIALVE, B., BERNET, N. & BERNARD, O. 2009. Anaerobic digestion of microalgae as a necessary step to make microalgal biodiesel sustainable. J.Biotech adv, 27, 409-16

## Slide 3: Calorific Value of Methane
John J Milledge

## Slide 4: A Simple Reaction
CH4 + 2O2 = CO2 + 2H2O
What is the problem?

## Slide 5: Calorific Value; Higher or Lower ?
Heat of Combustion
The calorific value of a fuel is the energy released by a unit quantity of fuel on complete combustion.
Higher Calorific Value (Gross) is the value obtained when all the water vapour has been condensed
EASTOP, T. D. & MCCONKEY, A. 1970. Applied Thermodynamics for Engineering Technologists, New York, Longman.

## Slide 6
Lower Calorific Value (Net) assumes all the water from the reaction remains as water vapour.
Enthalpy Water
    ∆Hliquid= 285.83kJ mol-1 ∆Hgas =241.83kJ mol-1
    Energy released on condensation = 44kJ mol-1
2 moles of H2O are generated from the combustion of 1mole of CH4
Difference between HCV & LCV ≈ 88kJ mol-1
NIST Standard Reference Data . http://webbook.nist.gov/cgi/cbook.cgi?ID=C7732185&Units=SI&Mask=1#Thermo-Gas

## Slide 7: Lower Calorific Value
In older boiler systems the latent heat from the condensation of water vapour was not recovered.

## Slide 8: Modern Systems attempt to recover the latent energy of water vapour

## Slide 9: Higher Calorific Value
Higher Calorific Value is widely used by the Department of Energy and Climate Change and UK National Statistics.
http://www.statistics.gov.uk/hub/business-energy/energy/energy-prices

## Slide 10: Food. Calorific Value
Protein is incompletely oxidised in the body . Nitrogen together with some carbon and hydrogen leave the body mainly in form of urea.
1.25 kcal are often deducted from the heat of combustion of protein for un-oxidised products excreted in urine
Total Nitrogen is often used to calculate protein.
MERRILL, A. L. & WATTS, B. K. 1955. Energy values of foods: Basis & Duration. Slight revised February 1973. US Department of Agriculture. Available on line at http://www.nal.usda.gov/fnic/foodcomp/Data/Classics/ah74.pdf

## Slide 11: Methane Heat of Combustion per Mole HCV
ΔcH°gas ≈ -890.16 to -891.8kJ mol-1
NIST Standard Reference Data. http://webbook.nist.gov/cgi/cbook.cgi?ID=C74828&Mask=1#Thermo-Gas (
ΔcH°gas ≈ -212.8 kcal mol-1 @25C
ΔcH°gas ≈ - 891.0 kJ mol-1
GLASSTONE, S. & LEWIS, D. 1970. Elements of Physical Chemistry, London, MacMillan. (
ΔcH°gas≈ - 890.63 kJ mol-1 @25C
ΔcH°gas ≈ - 892.97 kJ mol-1 @0C
BSI 2005. Natural gas - Calculation of calorific values, density, relative density & Wobbe index from composition. BS EN ISO 6976:2005.
kilocalorie = 4.1868kJ PERRY, R. H. & CHILTON, C. H. 1973. Chemical Engineers' Handbook, Tokyo, McGraw Hill.

## Slide 12: Enthalpy Calculation
Energy release = Enthalpy of the products less Enthalpy of reactants
CH4(g) + 2O2(g) = CO2(g) + 2H2O(l)
CO2(g) -94.05
2H2O(l) ( 2 x 68.31) -136.64
CH4(g) 17.80
2O2(g) 0.0
Heat of Combustion (891.33kJ/mole) -212.89 kcal mol-1 NIST Standard Reference Data. http://webbook.nist.gov/cgi/cbook.cgi?ID=C74828&Mask=1#Thermo-Gas 298.15K 1bar

## Slide 13: Bond Energy Calculation CH4 + 2O2 = CO2 + 2H2O
Reactants
C-H 98 CH4 =98 x 4 392
O=O 118 2O2 = 2 x 118 236
628
Products
C=O(CO2) 192 CO2 = 192x 2 384
O-H 110 2H2O = 110 x 4 440
824
Lower Calorific Value (Exothermic) (25C) -196Kcal/mole
GLASSTONE, S. & LEWIS, D. 1970. Elements of Physical Chemistry, London, MacMillan.
Michigan State University. http://www2.chemistry.msu.edu/faculty/reusch/VirtTxtJml/react2.htm

## Slide 14: Bond Energies are average bond enthalpies for the gaseous state
Difference between HCV & LCV ≈ 88kJ mol-1
21.2 kcal mol-1
Calculated HCV from bond energy=
196 + 21.2 = 217.2 kcal mol-1 (909.4kJ mol-1)

## Slide 15: Temperature & Pressure
Boyle’s law; The volume of a gas varies inversely with its pressure at constant temperature
Charles’ Law (Gay- Lussac’s Law); The volume of a gas at constant pressure varies in direct proportion to the absolute temperature.
Avogadro’s Law; Equal numbers of molecules of different gases will occupy the same volume at a given temperature and pressure.

## Slide 16: Ideal Gas Law
PV = nRT
P, V and T are the pressure, volume and absolute temperature.
n is the number of moles of gas
R is the universal gas constant . I mole of gas occupies 22.414L at STP (273.15K at 1 atmosphere)  R is 0.082 litre atmosphere per mole per degree Kelvin
R is the universal gas constant . I mole of gas occupies 22.71108L at STP (273.15K at 1 bar)  R is 8.314472 J K-1 mol-1
GLASSTONE, S. & LEWIS, D. 1970. Elements of Physical Chemistry, London, MacMillan.
SAWYER, C. N. & MCCARTY, P. L. 1967. Chemistry for Sanitary Engineers, New York, McGraw Hill.
http://www.iupac.org/publications/books/gbook/green_book_2ed.pdf

## Slide 17: Ideal Gas
No Gas behaves ideally
Fortunately all gases approach ideal behave as pressure decreases

## Slide 18: Real Gas
For the purposes of the International Standard (BS EN ISO 6976:2005) the real-gas calorific value on a molar basis is taken as numerically equal to the corresponding ideal-gas value.
NOTE In practice, this correction is very small for typical natural gases, and can usually be neglected with resultant errors approximately 0.005 %
BSI 2005. Natural gas - Calculation of calorific values, density, relative density & Wobbe index from composition. BS EN ISO 6976:2005

## Slide 19: Standard Temperature & Pressure
“When gas volumes are reported as corrected to standard temperature and pressure (STP), more often than not the standard conditions are not given.
There are currently several definitions of STP in widespread use, with standard temperatures between 0 and 25 °C and standard pressures between 100 and 101.325 kPa, quoted in a variety of units.
As an extreme example, using the former International Union of Pure and Applied Chemistry definition of 0 °C and 101.325 and the National Bureau of Standards definition of 25 °C and 100 kPa gives a volume difference of more than 10% for the same mass of gas.”
WALKER, M., ZHANG, Y., HEAVEN, S. & BANKS, C. 2009. Potential errors in the quantitative evaluation of biogas production in anaerobic digestion processes. Bioresource Technology, 100, 6339-6346.

## Slide 20: Gas Metering Temperatures
            T1 T2
Japan 0 0
China 20 20
Germany 25 0
United Kingdom 15 15
USA 15 15
T1/C = combustion reference temperature
T2/C = volumetric or metering reference temperature
The reference pressure is 101,325 kPa in all cases
BSI 2005. Natural gas - standard reference conditions. BS EN ISO 13443:2005.

## Slide 21: Gas Production Temperature
Mesophilic digestion
Thermophilic digestion
35.6kJ L-1 HCV at 35C

## Slide 22: Standard Temperature Pressure
Oxford Dictionary Science Definition
“STP Standard Temperature Pressure formerly known as NTP (Normal Temperature and Pressure). The standard conditions used as a basis for calculations involving quantities that vary with temperature and pressure. These conditions are used when comparing the properties of gases. They are 273.15K (0C) and 101325Pa (or 760mmHg)”
DAINTITH, J. & MARTIN, E. (eds.) 2010. A Dictionary of Science Oxford Oxford University Press

## Slide 23: Standard Pressure
STP of 0C (273.15 K) and 101.325 kPa
is the old IUPAC standard
http://old.iupac.org/goldbook/
http://www.iupac.org/goldbook/S05910.pdf
IUPAC recommends that the former use of the pressure of 1 atm as standard pressure (equivalent to 1.01325 x 105 Pa) should be discontinued and now suggests a pressure for STP 105 pascals (1bar)

## Slide 24: BS & ISO Standard Pressure
A Pressure of 101.325 kPa (1 atmosphere) is widely used in ISO standards and in particular those concerned with Natural Gas and Methane.
BSI 2005a. Natural gas - Calculation of calorific values, density, relative density & Wobbe index from composition. BS EN ISO 6976:2005.
BSI 2005b. Natural gas - standard reference conditions. BS EN ISO 13443:2005.

## Slide 25: Joules Law
The internal energy of a ideal gas is a function of absolute temperature only.
At any constant temperature the internal energy is independent of its volume.
H = U + pV if U constant ∆H = ∆p∆V
= (101325-100000)(0.022413996-0.0 2271108 )
≈0.4 Joules
Although Methane, is not an ideal gas the change in heat of combustion per mole between the two suggested standard pressure is very small less than 1 joule per mole

## Slide 26: Higher Calorific Value of Methane Courtesy of Sonia Heaven
 | MJ kg-1 | g mol-1 | Mol litre-1 | MJ m-3
CH4 | 55.662 | 16.04 | 22.414 | 39.84
H2 | 141.79 | 2.01588 | 22.414 | 12.75
C | 12.011 |  |  | 
H | 1.00794 |  |  | 
CH4 | 16.04276 |  | 0.715747 | g CH4 l-1
CV from BS EN ISO 6975 at 0 C on a mass basis
Weiser, M.E. (2007) Atomic Weights of the Elements 2005. J. Physical and Chemical Reference Data 36, 485 (2007); doi:10.1063/1.2717223
22.413 996(39) × 10-3 m3·mol-1 with relative standard uncertainty 1.7 × 10-6, at 273.15 K and 101.325 kPa
Mohr, P.J., Taylor, B.N., Newell, D.B. (2008) CODATA Recommended Values of the Fundamental Physical Constants: 2006. Reviews of Modern Physics 80: 633–730

## Slide 27: Begin at the beginning and go on till you come to the end: then stop.
LEWIS CARROLL, Alice in Wonderland